## Slide 1
Robert Colwell
R&E Colwell & Assoc. Inc.
Thoughts on
Comp Arch Futures
Why does this guy
look so worried?
Oh.

## Slide 2: My Perspective on Computer Architecture Research
Is not about instruction sets or ISAs
Has sometimes been about systems & interconnects
Biggest payoff has been microarchitectures for 35+ years
Winning formula
  Think of a new tweak, simulate in isolation for perf impact
    If big enough, include in design or write paper
  Accumulate ideas into new product
  Apply “windage”
    Experienced designers judge sims down: implementation issues or “feature crosstalk”
    If publishing, leave out, hope referees don’t notice (they probably won’t)
  Don’t go too far or cost, complexity or schedule slips will sink you
  Repeat until out of time, then tape out

## Slide 3: Classic Microarchitecture Paradigm No Longer Works
It has several serious flaws going forward.
It presumes that perf improvements are all that matter for winning product
  This has not been true for at least 10 years
It does not account for opportunity costs
  New ideas cost
    Design time
    Chip real estate
    Degradation of other features
  But mainly it ignores power dissipation, and you can no longer (ever) do that

## Slide 4: uArch Perf Tweaks Mean Nothing In Isolation Any More
My new Total Speculation Cache makes my design 12.4% faster.
You are an idiot.

## Slide 5: Don’t Get Trapped in the Horizontal Mindset
Computer systems are extremely complex.
You are taught to think of them in horizontal layers
Apps at top
OS under that
Instruction set arch
Microarchitecture
Circuits
Gates/devices (and so on)
But electronic systems don’t care how you think of them. They must work correctly at all levels, all the time. And they will only do that if you design them so they can’t possibly do anything else.
You must be able to transcend the horizontal mindset.

## Slide 6: Future Good Ideas in Comp Arch Must Comprehend…
  Power
  Energy & cooling
  Signalling
  Errors from worsening CMOS
  Huge, bloated SW and/or buggy apps
  Battery form factors, weight, lifetime, recharging
  Packaging
  EMI, RFI, radiation
  Unbalanced systems from unbalanced components
    very slow DRAM, low bandwidth I/O
  High cost pressure from impending commoditization
  And the end of Moore’s Law

## Slide 7: Where to look, what to consider
Ask the right questions
  What do buyers really want?
    They don’t want to buy computers, they buy solutions
    Faster isn’t always better
  Where should computations be done?
    Locally?
    Cloud?
  How should computations be done?
    No more {bits; ops; movement} than necessary
    No faster than necessary
    Would approximate solutions work?
    Find right balance in heterogeneous system (and learn to program it!)
  What will your new product do that’s never been possible before?
Most Importantly
  It isn’t technology that rules the computer kingdom.
  It’s economic$.

## Slide 8: Last Words, far beyond computer architecture
Don’t believe everything you hear today from us “old guys”
  If instruction set design is your passion, I think you’re nuts, but go prove me wrong and I’ll salute you
We all have our blind spots
  Your job is to avoid ours so you can have your own
Note that this talk assumed no new technology would come online
  That was on purpose to show what a blind spot looks like
  That’s my story and I’m sticking to it
The more certain we old guys are, the more skeptical you should be
  I’m sure of that

## Slide 9: The End